## Slide 1: An Introduction to Failure Modes and Effects Analysis (FMEA) Implementation at a Middle Georgia Manufacturing Facility
Dr. Joan Burtner
Fall 2009

## Slide 2: Failure Modes and Effects Analysis – Severity Ratings
Severity of Effect (10-1)
  Hazardous without warning
  Hazardous with warning
  Loss of primary function
  Reduced primary function performance
  Loss of secondary function
  Reduced secondary function performance
  Minor defect noticed by most customers
  Minor defect noticed by some customers
  Minor defect noticed by discriminating customers
  No effect

## Slide 3: Failure Modes and Effects Analysis – Occurrence Ratings
Likelihood of Occurrence
  9 Very High: Almost inevitable
  7 High: repeated failures
  4 Moderate: Occasional failures
  2 Low: Relatively few failures
  1 Remote: Failure is unlikely

## Slide 4: Failure Modes and Effects Analysis – Detection Ratings
Ability to Detect (10-1)
  Cannot detect
  Very remote chance of detection
  Remote chance of detection
  Very low chance of detection
  Low chance of detection
  Moderately high chance of detection
  High chance of detection
  Very high chance of detection
  Almost certain detection

## Slide 5: Risk Priority Number Calculations
Paint Material – accident or transport failure
  Potential Failure Effect
    Lack of paint consistency
    Severity of Effect rating 4
  Potential Cause
    Dropped powder
    Likelihood of Occurrence rating 3
  Current Control
    Lifting procedures
    Ability to Detect rating 3
Severity*Likelihood*Detection = 36 = RPN

## Slide 6: FMEA Example
Process Step/Part Number | Potential Failure Mode | Potential Failure Effects | SEV | Potential Causes | OCC | Current Controls | DET | RPN
MATERIAL | Power Outage | Plant Down | 6 |  | 6 |  | 6 | 216
MACHINE | Air Compressor Failure | Plant Down | 6 |  | 5 |  | 7 | 210
MATERIAL | Out of Paint Raw Material | Fab Down | 5 |  | 8 |  | 4 | 160
MACHINE | Mill water pump goes down | Plant Down | 6 |  | 3 |  | 8 | 144
EMPLOYEE | People not on the floor | Plant Down | 2 |  | 10 |  | 6 | 120
MACHINE | Boiler Down | Fab Down | 3 |  | 6 |  | 6 | 108