## Slide 1: Process and Performance Capability Assessment
Dr. Joan Burtner, Certified Quality Engineer
Borror, ed., The Certified Quality Engineer Handbook 3rd edition - Chapter 38

## Slide 2: Process Capability: Informal vs. Formal
Informal process capability assessment
  Is process capable of meeting certain requirements?
  Uses histograms, probability plots, stem-and-leaf plots
  Does not use stated specification limits
  Usually a quick assessment
Formal process capability study
  More time intensive than an informal assessment
  Requires characteristics that have specification limits
  Performed on “the characteristics that experience has shown to be difficult to hold to specification” Borror page 527

## Slide 3: Process Capability vs. Process Control
Process capability with respect to specifications
  Is process capable of meeting tolerances?
    Does the process conform to specifications?
  Potential problems
    The process is off-center from the nominal.
    The process variability is too large relative to the tolerances.
    The process is off-center and has large variation.
Process is “in-control” without respect to specifications
  Only common cause variation in range
  Only common cause variation in mean
  No violations of tests for control chart interpretation

## Slide 4: Process Capability Indices
A Process Capability Study is appropriately conducted only on processes after they have been shown to be “in-control”
Two standard indices
  Cp
    Compares variability of process to specifications
  Cpk
    Compares variability of process to specifications
    Considers the question: “Is the process sufficiently centered?”

## Slide 5: Calculation of Standard Process Capability Indices
Calculations
Estimated values
See Borror (pp 529-531) for worked examples

## Slide 6: Control Chart Constants
Subgroup Size | d 2 |  |  | A 2 | D 3 | D 4
2 | 1.128 |  |  | 1.880 | 0 | 3.267
3 | 1.693 |  |  | 1.023 | 0 | 2.575
4 | 2.059 |  |  | 0.729 | 0 | 2.282
5 | 2.326 |  |  | 0.577 | 0 | 2.115
6 | 2.534 |  |  | 0.483 | 0 | 2.004
7 | 2.704 |  |  | 0.419 | 0.076 | 1.924

## Slide 7: Standard Process Capability Evaluation Guideleines
Guidelines for Evaluation of Cp
  Cp < 1.00 Not Capable
Guidelines for Evaluation of Cpk
  Cpk > 1.33 Definitely Capable
  1.00 < Cpk < 1.33 Possibly Capable
  Cpk < 1.00 Not Capable

## Slide 8: Additional Process Capability and Process Performance Indices
 | This is the capability ratio. Smaller is better.
 | Provides a better measure of centering. See equation on page 532.
 | Use these process performance indices when process is NOT in statistical control. Substitute sample standard deviation for sigma. This is a controversial recommendation. (page 533)