## Slide 1: Monitoring Fetal Health
W. Scerbo, M., & Z. Abuhamad, A. (2015). Monitoring Fetal Health. Retrieved February 4, 2015, from http://webmm.ahrq.gov/case.aspx?caseID=338
ISE 468/ETM 568: Healthcare Process Improvement
Ana Carolina Rosa and Hevelyne Duarte de Souza

## Slide 2: The Case
A 29-year-old woman had an uncomplicated pregnancy with healthy fetus, and presented to the hospital with 40 weeks.
But when the infant was born, he was cyanotic and flaccid with very low Apgar scores. An arterial blood gas at the time showed a pH of 6.70 (normal: 7.25–7.35), a profound acidosis. The infant required extensive resuscitation but survived and was transferred to the neonatal intensive care unit.
The infant had brain injury from inadequate oxygenation of the brain that occurred during childbirth and other problems related to the complicated delivery.
“The fetus had been monitored using the standard fetal heart rate tracings throughout the time of labor. The fetal heart rate tracings had shown evidence of Category 2 and 3 abnormalities (moderate-to-severe fetal distress) for at least 90 minutes prior to the delivery. These abnormalities, which likely would have prompted an urgent cesarean delivery, had not been recognized by any of the physicians or nursing staff.”(p.1)
In this institution, continuous fetal heart monitoring of all of the women in labor was displayed centrally on a large 40-inch monitor; on this screen 16 rooms were displayed continuously on it and with two nurses watching it.
Notes: Apgar Score: It is a test designed to quickly evaluate a newborn's physical condition and to see if there's an immediate need for extra medical or emergency care. And is an acronym for: Appearance, Pulse, Grimace, Activity, and Respiration

## Slide 3: The Comentary
This case involves failure to recognize concerning fetal heart rate (FHR) tracings during labor;
“FHR activity and maternal contractions are recorded by transducers placed on the maternal abdomen and tracings can be displayed either on a paper strip or a computer screen” (p.2);
The baseline heart rate is measured in beats per minute (bpm) and measured over a 10-minute period;
Normal mean values for FHR : range from 110 to 160 bpm;
Deviations in the baseline activity are classified as:
  Absent (no noticeable bpm variation);
  Minimal (up to 5 bpm);
  Moderate (variability ranges from 6 to 25 bpm);
  Marked (exceeding 25 bpm).

## Slide 4: Categories of FHR
  The National Institute of Child Health and Human Development (NICHD) recently presented a new classification of FHR monitoring
  Intent is to standardize communication among health care providers and stratify fetal risk;
  Risk is classified as:
    Category 1: normal fetus
    Category 2: intermediate risk requiring close observation and monitoring
    Category 3: possible fetal compromise

## Slide 5: Technological advancements on monitoring FHR
Analog devices were located at the patient's bedside. Signals were traced with a pen onto a printed grid on paper that scrolled at a standard rate
Digitalized signals are presented on a computer screen and can be monitored from a remote location - usually placed in the nursing suite of the labor and delivery unit—because it allows many patients to be monitored simultaneously in a single location (centralized)
Notes: The rationale behind placing many FHR monitors in one central location is that it would facilitate monitoring of all patients simultaneously. Previously when FHR tracings occurred only at the bedside, a nurse or physician would have to visit the bedside frequently, and it was not possible to continuously monitor all patient tracings for signs of fetal distress. It was believed that centralized, continuous monitoring of all patients could lead to better outcomes.

## Slide 6: Differences
The digitization of FHR signals allows one or more tracings to be displayed on a standard computer screen
  In this case, data from 16 patients were displayed on a single 40-inch monitor, each tracing would be limited to about a 10-minute window of activity (assuming a 4 x 4 matrix); on the other hand, traditional paper tracings enables a clinician to scan 30 minutes or more of activity.
Notes: If the system allows selection and expansion of an individual patient's tracing, that can only be accomplished by obscuring, degrading, or reducing the size of other patient's tracings because the screen display size is limited.

## Slide 7: Differences
Related to the attentional challenges to monitor the displays.
  Vigilance decrement: the ability to maintain attention and respond to stimuli over long periods of time.
  Monitoring multiple displays or multiple sources of information depicted within a single display also tends to harm performance.
  In one study, observers asked to monitor multiple displays detected fewer signals and had more false alarms than those observing only a single display, because of that equipment designers should try to avoid creating displays with multiple components that need to be monitored.

## Slide 8: Safety Culture on Labor and Delivery Units
This complicated patient flow requires dedicated specialized teams with strong commitment to safety.
“Having a centralized monitoring station with insufficient number of available, well trained, vigilant, and undistracted personnel to monitor can be a recipe for bad outcomes.”(p.4)
Triage
Labor room
Delivery/Operating room
Recovery room
Notes: Labor and delivery is a busy environment, which involves patient transitions from triage to a labor room, to a delivery or operating room, and a recovery room. This complicated patient flow requires dedicated specialized teams with strong commitment to safety.

## Slide 9: Simple solutions to improve the detectability of critical signals and minimize vigilance decrements
Additional training;
Having more than one person monitoring the displays;
Limiting the duration of watchkeeping shifts.
More sophisticated possibilities:
  amplifying the signals
  using systems that provide warnings generated by computerized analysis of the FHR tracings
Notes: These methods have been applied in other high-risk domains (e.g., aviation, processing plant operations) and have reduced vigilance failures but not eliminated them completely.

## Slide 10: Conclusion
“Fetal heart rate monitoring on labor and delivery is a complex process that is often affected by staff education and training, staffing levels, and the unit safety culture.
Centralized monitoring introduces significant changes in the way patients are monitored. These changes are accompanied by some obvious advantages and some less obvious disadvantages.
Attempts to combat monitoring deficits in other high-risk domains with more sophisticated technology have reduced but not eliminated failures of attention.
Improving communication on the labor and delivery unit and establishing an ultra safe and resilient culture that promotes transparency are two major components of accurate interpretation of FHR.” (p.5)

## Slide 11: Reference
http://webmm.ahrq.gov/case.aspx?caseID=338